## Slide 1
End-to-End VM Connectivity Across Subnets Using sshuttle, WireGuard, and Static Routing
Presented by Visesh Bentula

## Slide 2
  sshuttle is a user-space VPN-like tool that forwards TCP traffic over an existing SSH connection.
  It works by intercepting traffic on one node and tunneling it transparently through another node.
  Advantages: quick setup, no need for root-level routing changes, useful for debugging or bypassing firewall restrictions.
  Limitation: only supports TCP traffic; does not handle UDP or ICMP packets (e.g., ping).
  Conceptually, sshuttle is a lightweight alternative to static routing or VPNs.
What is sshuttle?
01

## Slide 3
  WireGuard is a modern, high-performance VPN protocol designed to be simple yet highly secure.
  It creates an encrypted point-to-point tunnel using a small set of cryptographic primitives.
Advantages:
  Strong encryption with minimal overhead
  Supports all traffic types (TCP, UDP, ICMP)
  Faster and easier to configure compared to traditional VPNs
  WireGuard is widely used in production networks and is well-suited for research testbeds like FABRIC.
What is WireGuard?
02

## Slide 4
  Static routing is the manual configuration of network paths using commands like ip route.
  Each node is explicitly told which gateway to use to reach another subnet.
  Advantages: full control, transparency, works for all protocols without tunneling overhead.
Limitations:
  Not encrypted (unlike WireGuard)
  Inflexible, any change in the network requires manual updates.
  Conceptually, static routing is like a hard-coded map that ensures traffic flows in a predictable way
What is Static Routing?
03

## Slide 5
FABRIC Setup (Token & Slice Creation)
01
02
04
Presentation 2024
Thynk Unlimited
Project
-
-
After completing the setup, I proceeded by following the research methodology and step-by-step process outlined in the project artifacts
Token = authentication key, Slice = mini network lab

## Slide 6
sshuttle Results
What Worked:
  sshuttle created an SSH-based tunnel through Node2
  A dummy route allowed Node1 to reach Node3’s subnet
  Node1 successfully connected to Node3 (TCP port 22)
  Routing table showed traffic for 192.168.2.0/24 redirected via 127.0.0.1
What Failed / Limitation
  sshuttle only supports TCP traffic
  Does not handle ICMP (ping) or UDP
Conclusion:
  sshuttle provided quick TCP connectivity with minimal setup
  Best suited for debugging or temporary access, not full connectivity
05

## Slide 7
WireGuard Results
What Worked:
  Node1 ↔ Node3 tunnel communication (10.0.0.x) successful
  Node1 reached Node3’s underlay (192.168.2.2)
  TCP test confirmed SSH connectivity on port 22
What Failed (100% Packet Loss):
  Node3 could not ping Node1’s underlay (192.168.1.1)
  Cause: WireGuard only forwards traffic defined in AllowedIPs
  Node2 lacked forwarding/NAT rules to bridge overlay → underlay
Conclusion:
  The packet loss is expected, not an error in WireGuard
  To fix: enable forwarding/NAT on Node2 to allow overlay traffic to reach underlay IPs
06

## Slide 8
Static Results
What Worked
  WireGuard and sshuttle were stopped to avoid interference
  Node2 was configured with IP forwarding, acting as a router
  Static routes set via Node2’s interfaces:
  Node1 → Node3 via 192.168.1.2 (Node2)
  Node3 → Node1 via 192.168.2.1 (Node2)
  Ping confirmed connectivity between Node1 (192.168.1.1) ↔ Node3 (192.168.2.2)
  Routing tables showed correct static entries pointing to Node2
What Failed / Limitation:
  No encryption — traffic flows in plain text
  Routes must be updated manually if the network changes
Conclusion:
  Static routing delivered reliable end-to-end connectivity through Node2
  Useful for learning and controlled experiments, but less secure and flexible than WireGuard
07

## Slide 9
Presentation 2024
Thynk Unlimited
Project
-
-
Thank You